# Diffraction by wire

OBJECT: To find the wavelength of laser using a thin wire of unknown thickness.

Apparatus used: He-Ne laser with stand and power supply, measuring scale.

Formula used: When a thin wire is introduced in the path of the laser beam, the beam undergoes diffraction similar to the two-slit Fraunhofer diffraction. If the thickness of the wire is d, then the angular position ( for the 1st minima on either side is given by

d Sin( = (/2

Now, if the distance between the wire and the screen is D, and the width of the central maxima is b, assuming the angle ( to be small, we can write

Sin( ( ( ( b/2D

Which gives the wavelength of the laser light as:

# Procedure:

- Switch on the laser and wait till the beam stabilizes. Align the laser beam horizontally so that it may fall on wire properly.

- Place the wire symmetrically in the path of the beam. Keep the distance between screen and the wire sufficiently large (≈1m).

- Place paper on the screen and mark the points corresponding to the maxima.

- Carefully measure the distance between the points with the help of vernier calipers.

- Repeat the experiment for three different distances between wire and screen.

- Calculate the wavelength in each case and find the average wavelength of laser beam.

Observation:

Least count of the vernier calipers =

Least count of the measuring scale =

Thickness of the wire d		 =

Table for finding out the wavelength of laser beam

| Sr. No. | Distance of the wire from the screen D | Width of the Central Maxima b | Wavelength of the laser beam | Mean Wavelength |
| --- | --- | --- | --- | --- |

Result:

The wavelength of the He-Ne laser is….………….Å

Precautions:

- The position of the laser and the wire is not to be disturbed throughout the experiment.

- Avoid direct eye exposure to the laser radiation.